## Slide 1: Fast Timing-driven Partitioning-based Placement for Island Style FPGAs
Pongstorn Maidee, Cristinel Ababei, Kia Bazargan
Electrical and Computer Engineering Department
University of Minnesota
{pongstor,ababei,kia}@ece.umn.edu

## Slide 2: Significance?
FPGA increasingly more popular
  Rapid prototyping
  Shorter time-to-market for end products
  Small non-recurring costs
  Late debugging possible
  Relatively easy design flow
CAD tools have to catch up
  Faster, scalable algorithms
  FPGA specific physical design

## Slide 3: Problem?
FPGA Placement
  Long runtimes
  More iterations to converge
Example: 11648 CLBs placed ~ 3 days by VPR

## Slide 4: Previous approaches
Placement using annealing
  Example: VPR
  + : Best quality
  – : Long runtimes
  – : Placement & routing not well correlated
Runtime/Quality tradeoff
  Example: UltraFast [J. Rose FPGA’99]
  + : Tunable runtime
  – : Quality degradation

## Slide 5: Previous approaches
Parallel implementations
  Examples: [D. F. Wong FPGA’03], [DeHon FPGA’03]
  + : Tunable runtime with # processors
  – : Complicated implementation
  – : Inferior in quality

## Slide 6: FPGA characteristics
Routing
  Segmented tracks
  Switches
Delay model
  Wire length / bounding box NOT accurate
    Same BBox, fewer segs  smaller delay
  Alignment:
    H/V aligned nets better than L-shaped nets

## Slide 7: Proposed approach
Top-down partitioning-based placement
  Fast (divide&conquer)
Delay estimation
  Empirical routing delay analysis
  Correlate net criticality and routing resource usage
Delay optimization
  Align critical connections
  Dynamically update net delays
Long
L6
L2
L1
?
?

## Slide 8: Outline
Framework
Net terminal alignment
Delay assignment
Refinement step
Results
Summary

## Slide 9: Partitioning-based Placement
Initial analysis
Routing Profiles
Recursive bipartitioning
  hMetis
  Terminal alignment
  Delay budget re-assignment
Level
1
2
2
3
3
3
3
Terminal alignment
Partitioning-based placement
Next level
Delay Assignment
Refinement
Overlap Removal
VPR Low-temp annealing
VPR Routing

## Slide 10: Partitioning Order
1
2
3
4
5
6
7
Column by column, and left-to-right.
Is this the best way?
to be partitioned placement regions
partitioned placement regions

## Slide 11: Outline
Framework
Net terminal alignment
Delay assignment
Refinement step
Results
Summary
Routing Profiles
Level
1
2
2
3
3
3
3
Partitioning-based placement
Next level
Delay Assignment
Overlap Removal
VPR Low-temp annealing
VPR Routing
Terminal alignment

## Slide 12: Net terminal alignment
Multi-terminal  two-terminal
A or B?
Alignment helps reduce # routing segments
Y anchor point
X  A preferred (one segment possible)
A
B
already cut
about to be cut
Y
X
X

## Slide 13: Cut Direction?
For X:
  {A,C} preferred to {B,D}
  Then, C preferred to A
A
B
already cut
about to be cut
C
D
crit = 0.4
crit = 0.4
crit = 0.9
crit = 0.5
Conflict between different nets
  Net criticality decides
Y
X
X

## Slide 14: Alignment Details
Align a node if:
  Has an anchor
  Is timing critical
  Anchor in the same direction as the cut
regions already
placed at same
level
Free
Critical anchor
Non-critical anchor
Fixed

## Slide 15: Alignment Details
Align a node if:
  Has an anchor
  Is timing critical
  Anchor in the same direction as the cut
regions already
placed at same
level
Free
Critical anchor
Non-critical anchor
Fixed

## Slide 16: Alignment Details
Align a node if:
  Has an anchor
  Is timing critical
  Anchor in the same direction as the cut
regions already
placed at same
level
Free
Critical anchor
Non-critical anchor
Fixed

## Slide 17: Partitioning Order Revisited
Top-to-bottom and left-to-right.
1
2
3
4
5
6
to be partitioned placement regions
partitioned placement regions
To be horizontally aligned
To be vertically aligned

## Slide 18: Outline
Framework
Net terminal alignment
Delay assignment
Refinement step
Results
Summary
Routing Profiles
Level
1
2
2
3
3
3
3
Terminal alignment
Partitioning-based placement
Next level
Overlap Removal
VPR Low-temp annealing
VPR Routing
Delay Assignment

## Slide 19: Delay Estimation
Delay hard to estimate
  Top-down framework
    At higher levels, no accurate location information
  FPGA architecture
    Several segment types available
Correlation analysis
  Min distance estimation  segment type usage
    Level of partitioning  min dist
  Net criticality  segment type usage

## Slide 20: Analysis: Seg Types  Level
Perform placement & routing
apex2
Hierarchy level
Segment Usage
2
4
1000
2000
Count segment types crossing level 1 boundaries

## Slide 21: Analysis: Seg Types  Level
Perform placement & routing
apex2
Hierarchy level
Segment Usage
2
4
1000
2000
L6
Long
L2
L1
Count segment types crossing level 1 boundaries

## Slide 22: Analysis: Seg Types  Level
Perform placement & routing
apex2
Hierarchy level
Segment Usage
2
4
1000
2000
L6
Long
L2
L1
Count segment types crossing level 1 boundaries
Repeat for other levels

## Slide 23: Analysis: Seg Types  Level
Perform placement & routing
apex2
Hierarchy level
Segment Usage
2
4
1000
2000
L6
Long
L2
L1
Count segment types crossing level 1 boundaries
Repeat for other levels

## Slide 24: Analysis: Seg Types  Level
Perform placement & routing
apex2
Hierarchy level
Segment Usage
2
4
1000
2000
L6
Long
L2
L1
Count segment types crossing level 1 boundaries
Repeat for other levels

## Slide 25: Analysis: Seg Types  Level
Perform placement & routing
apex2
Hierarchy level
Segment Usage
2
4
1000
2000
L6
Long
L2
L1
Count segment types crossing level 1 boundaries
Repeat for other levels

## Slide 26: Slack, Distance, Delay
Data shows delay as a function of net criticality and distance
Delay is net delay after VPR routing
Each point the average over all nets falling in the (dist, crit) range.

## Slide 27: Delay Estimation
  Blue terminals: 3
Level k
: size of a region
Calculate [min, max] dist
Example:

Delay assignment
  Length + # of bends
  Criticality
  Red terminals: (3+2)+ 

## Slide 28: Outline
Framework
Net terminal alignment
Delay assignment
Refinement step
Results
Summary
Routing Profiles
Level
1
2
2
3
3
3
3
Terminal alignment
Partitioning-based placement
Next level
Delay Assignment
Overlap Removal
VPR Low-temp annealing
VPR Routing

## Slide 29: Refinement step
At the end, some regions over-crowded
Greedy overlap removal approach:
  Non-critical CLBs move
  Preserve alignments.
Low temperature SA (modified VPR)
  CLB swap distance is limited.
  Preserve alignments
  Start from a low temperature (~10% of the normal).

## Slide 30: Outline
Framework
Net terminal alignment
Delay assignment
Refinement step
Results
Summary

## Slide 31: Experimental Framework
Timing info
VPR Routing
Ckt netlist
VPR Placement
Goal:
  Verify the alignment idea
Flow:
  For each circuit, perform annealing placement
  Profile routing info
  Use the same profile in our placement flow
Application: redo placement to get better timing
VPR Routing
Our placement
Routing analysis

## Slide 32: Alignment Results
8 out of 10 circuits yield better delay.
3% better delay on average, max 9.5%
 Delay info is reliable.
Alignment effective
Runtime overhead compared to pure annealing: 15%
Circuit | PPFF | VPR
 | Delay | Delay
ex5p | 7.69 | 8.02
apex4 | 7.51 | 6.69
misex3 | 7.25 | 7.48
alu4 | 6.72 | 6.84
des | 9.51 | 9.52
seq | 8.12 | 8.10
apex2 | 8.33 | 8.91
spla | 12.3 | 13.6
pdc | 14.4 | 15.4
ex1010 | 13.8 | 15.1
Avg. | 0.97 | 1

## Slide 33: Experimental Framework
Timing info
VPR Routing
Selected circuits
VPR Placement
Goal:
  Verify our overall flow
Flow:
  Profile routing info on few circuits (ONE TIME)
  Use the profile in our placement flow
Application: fast placement, high quality
VPR Routing
Our placement
Routing analysis
Ckt netlist

## Slide 34: Results of Our Flow
Same average circuit delay.
Almost same total channel width.
Around 6 times faster
Circuit | PPFF |  |  | VPR |  | 
 | Delay | CW | CPU (s) | Delay | CW | CPU (s)
ex5p | 7.91 | 23 | 30 | 8.02 | 22 | 177
apex4 | 7.5 | 23 | 35 | 6.69 | 23 | 208
misex3 | 8.33 | 20 | 38 | 7.48 | 19 | 227
alu4 | 6.84 | 19 | 41 | 6.84 | 19 | 245
des | 9.4 | 22 | 60 | 9.52 | 22 | 382
seq | 7.66 | 23 | 51 | 8.1 | 23 | 432
apex2 | 7.87 | 22 | 56 | 8.91 | 22 | 370
spla | 13.2 | 30 | 154 | 13.6 | 30 | 1180
pdc | 15.1 | 32 | 221 | 15.4 | 32 | 1599
ex1010 | 15.2 | 22 | 210 | 15.1 | 22 | 1408
Avg. | 1 | 236 | 1 | 1 | 234 | x6.68
* Representative circuits shaded.
Notes: Avg delay is harmonic mean (arith mean: ours=.99)
Avg speedup is the arith mean of speedups

## Slide 35: Runtime Growth
size vs runtime
0
200
400
600
800
1000
1200
1400
1600
1800
0
1000
2000
3000
4000
5000
clb size
sec
PPFF
VPR

## Slide 36: Outline
Framework
Net terminal alignment
Delay assignment
Refinement step
Results
Summary

## Slide 37: Summary
Partitioning-based placement  fast
Place&route delay profiles  delay estimation
Alignment  better timing
Dynamic delay updates  better delay estimation
Annealing + partitioning-based 
  3% better timing
  15% runtime overhead
Partitioning-based only 
  ~ Same quality
  6x speedup

## Slide 38: Future work
Congestion
More accurate delay information
Eliminate low temperature annealing
Partitioning ordering

## Slide 39
Thank You!
Contact:
Kia@ece.umn.edu